Презентація
Виробничої практики
Мікропроцесорна модель збору і обробки інформації
Група ФЕІ - 51с
ст. Петришин Олег

---
Зміст
- Мікропроцесорна модель
- Структура мікропроцесорної моделі
- Презентаційний стенд

---
Мікропроцесорна модель
- Безпілотний прилад дистанційного керування, квадрокоптер.
- Автоматизована система регулювання висоти польоту квадрокоптера на основі висотоміра низьких частот.
- Система автоматичного передавання висоти та дистанційний запис польоту квадрокоптера.

---
Структура мікропроцесорної моделі
- Модель складається із набору двох мікроконтролерів різних архітектур.
- Один мікроконтролер відіграє роль передавача, інший — отримувача та записуваного пристрою польоту квадрокоптера.

---
Презентаційний стенд
Nordic Semiconductor
nRF24L01+
Single Chip 2.4GHz Transceiver
- Worldwide 2.4GHz ISM band operation
- 250kbps, 1Mbps and 2Mbps on air data rates
- Ultra low power operation
- 11.3mA TX at 0dBm output power
- 13.5mA RX at 2Mbps air data rate
- 900nA in power down
- 26µA in standby-I
- On chip voltage regulator 1.9 to 3.6V supply range
- • 5V tolerant inputs
Arduino Uno Atmega328P
- Clock Speed	16 Mhz 8-bit MCU
- Flash Memory	32 KB of which 0.5 KB used by bootloader
- SRAM	2 KB
- EEPROM	1 KB
- Operation voltage: 5V
PSoC 4 CY8C4245AXI
- 32-bit MCU Sub-system: 48-MHz ARM Cortex-M0 CPU with single cycle multiply
- Flash: 32 KB
- SRAM: 4 KB
- Interface Type:	I2C, SPI, UART
- Low Power 1.71-V to 5.5-V Operation